## Slide 1: Modeling and Validation of CN Violet Radiation Relevant to Titan Entry
Aaron Brandis
Andrew Hyatt, Grant Palmer
and Michael Wright

## Slide 2: Context
• To aid the design and selection of Thermal Protection Systems (TPS), measurements of radiation under conditions relevant to Titan entry have been made.
Shock heated test gas in experiment simulates conditions found behind the vehicle’s bow shock during entry.
Previous comparisons of shock tube radiation data have shown significant discrepancies compared to theory (design uncertainty of TPS can be as high as a factor of 2).
Understanding discrepancies may influence future margin policies.
Present analysis attempts to improve understanding of radiative heating for Titan entries.
Focus on non-equilibrium radiation as would be relevant to a mission aiming to splashdown on a Titan sea, such as TiME.
Notes: Shock speed, post shock pressure, atmospheric composition same as flight

## Slide 3: CN Radiation
Radiation during Titan entry more important at lower speeds (5 – 6 km/s) than other planetary entries due to formation of CN in above equilibrium concentrations.
Non-equilibrium concentration is formed through interaction of following reactions:
  N2 + M ↔ 2N + M
  N2 + C ↔ CN + N
  CN(X) + M ↔ CN(B) + M

## Slide 4: CN Radiation
Radiation during Titan entry more important at lower speeds (5 – 6 km/s) than other planetary entries due to formation of CN in above equilibrium concentrations.
Non-equilibrium concentration is formed through interaction of following reactions:
  N2 + M ↔ 2N + M
  N2 + C ↔ CN + N
  CN(X) + M ↔ CN(B) + M
Comprehensive understanding of these mechanisms and corresponding rates is required for an accurate prediction of Titan non-equilibrium radiation.

## Slide 5: Huygens Titan Studies
Several studies performed to investigate Titan radiative heating for Huygens/Cassini mission.
Boltzmann and Collisional Radiative (CR) models developed to simulate EAST experiments from NASA Ames.
Boltzmann was identified to significantly over-predict the radiation as measured by experiments, so it was concluded that CR models would be required.

## Slide 6: Huygens Titan Studies
The agreement between CR models and experiment for the peak was deemed to be satisfactory, however, significant discrepancies regarding the decay rate were observed.
Notes: Some reasons for questioning validity of these EAST results

## Slide 7: Procedure for Titan Heating Estimates
2-D axisymmetric capsule simulation using a coupled DPLR/NEQAIR solution to determine total body heat flux (both convective and radiative) based on Boltzmann assumptions.
Run 1-D Boltzmann and CR model to determine over-prediction factor of Boltzmann with respect to CR. This factor is then used to scale down the radiative component of the DPLR solution.
CR model compared to X2, confirm that the CR model is conservative with respect to the experimental data.

## Slide 8: CFD Titan Capsule Solutions

## Slide 9: CFD Titan Capsule Solutions
Notes: Run CR models corresponding to the stagnation point of the body

## Slide 10: Collisional Radiative Model
Flow Field computed by solving 1D conservation equations of mass, momentum, global energy, vibrational energy of N2 molecule
Collisional Radiative Model
    Predicts nonequilibrium levels of CN(A,B) and N2(A,B,C)
CR Model comprises:
  spontaneous emission of excited states
    eg: CN(B) -> CN(X) + hv
  collisional (de)excitation with nitrogen
    eg: CN(X) + N2 ↔ CN(B) + N2
  electronic impact (de)excitation
    eg: N2(X) + e- ↔ N2(B) + e-
  pooling
    eg: N2(A) + N2(A) ↔ N2(X) + N2(C)
  quenching
    eg: N2(A) + CN(X) ↔ N2(X) + CN(B)
Coupling effects are not included, however, as the radiation predicted by CR models is substantially less than Boltzmann, coupling effects become less significant.

## Slide 11: X2 Shock Tube
Free Piston driver used to build pressure and burst diaphragm
Radiation behind shock wave analyzed just after shock exits the tube
For Titan, spectral and spatially resolved CN emission has been observed over a range of conditions:
  From 4 – 7.6 km/s at 133 Pa (1 Torr)
  From 6 – 1000 Pa at 5.7 km/s
X2 condition of 5.7 km/s and 30 Pa, close to potential TiME peaking heating of 5.24 km/s and 28.5 Pa

## Slide 12: Comparison of X2 Data and Models Relevant to TiME
Reduction from Boltzmann to CR factor of ≈ 4.6
CR over-predicts X2 by factor ≈ 5
Boltzmann over-predicts X2 by factor of ≈ 23
5.7 km/s, 30 Pa,
310 – 470 nm

## Slide 13: Reduction in TiME Estimated Heat Flux
CR model is conservative compared to experimental data
Boltzmann over-predicts CR model by a factor of 4.6 for a condition measured on X2 similar to peak heating for TiME
Therefore, this factor can be used to reduce full flow field DPLR calculation using Boltzmann assumption and still be a conservative approach compared to experimental results
Boltzmann estimate at peak heating for Qrad = 78 W/cm2; with CN over-population correction based on CR model: Qrad = 17 W/cm2
Notes: Qconv = 77 W/cm2, corresponding to 40 – 50% reduction to total heat flux

## Slide 14: TiME Trajectory vs X2 Conditions
X2 conditions bound TiME conditions of interest with respect to heating
Notes: X2 vs CR new traj.xlsx

## Slide 15: 6.3 km/s, 30 Pa, 150 K
6.3 km/s, 60 Pa, 300 K
310 – 470 nm
Analogous to 6.3 km/s, 30 Pa, 150 K
Boltzmann over-predicts CR by 2.3 at peak
Notes: X2 vs CR new traj.xlsx

## Slide 16: 5.3 km/s, 60 Pa, 150 K
5.3 km/s, 120 Pa, 300 K
310 – 470 nm
Analogous to 5.3 km/s, 60 Pa, 150 K
Boltzmann over-predicts CR by 2.2 at peak

## Slide 17: 4.6 km/s, 90 Pa, 150 K
4.6 km/s, 180 Pa, 300 K
310 – 470 nm
Analogous to 4.6 km/s, 90 Pa, 150 K
Boltzmann over-predicts CR by 1.7 at peak

## Slide 18: X2 at 5.7 km/s, 60 Pa
5.7 km/s, 60 Pa, 300 K
310 – 470 nm
CR over-predicts X2 by 10.7 at peak

## Slide 19: Calibration Check for X2 Results
Titan has not been a focus of recent EAST testing.
In order to check the calibration of X2, it was decided to compare the results of equilibrium radiation for Mars with EAST and X2.
X2 result within scatter of EAST, and in good agreement with NEQAIR.
Notes: EAST_X2_NEQAIR.xlsx

## Slide 20: Calibration Check for X2 Results
Titan has not been a focus of recent EAST testing.
In order to check the calibration of X2, it was decided to compare the results of equilibrium radiation for Mars with EAST and X2.
X2 result within scatter of EAST, and in good agreement with NEQAIR.
X2 intensity calibration confirmed by comparison with EAST and NEQAIR
Notes: EAST_X2_NEQAIR.xlsx

## Slide 21: Effect of Rates on Radiance
5.15 km/s
13 Pa
310 – 450 nm
Notes: 5.7 and 5.15 kms with CR.xls

## Slide 22: Effect of Rates on Radiance
5.7 km/s
13 Pa
310 – 470nm
Notes: 5.7 and 5.15 kms with CR.xls

## Slide 23: Effect of Rates on Radiance
5.7 km/s
13 Pa
Using the Tsagi rate for CN(B) excitation & multiplying N2 dissociation rate by 10, excellent agreement has been obtained with X2.
Notes: 5.7 and 5.15 kms with CR.xls

## Slide 24: Nonequilibrium Analysis of X2
Parameter developed to quantify level of non-equilibrium found in either an experiment or simulation.
Designed to be independent of 1) experimental settings, such as gate with and spectrometer resolution and 2) the absolute intensity calibration.
Parameter grounded to equilibrium level of radiation.
Can be used for robust comparisons with simulations and for evaluating different reaction rates.

## Slide 25: Nonequilibrium Analysis of X2
Nonequilibrium parameter = Nonequilbrium Area / Equilibrium Level

## Slide 26: Nonequilibrium Analysis of X2
Nonequilibrium parameter = Nonequilbrium Area / Equilibrium Level
Nonequilibrium Area

## Slide 27: Nonequilibrium Analysis of X2
Nonequilibrium parameter = Nonequilbrium Area / Equilibrium Level
Nonequilibrium Area
Equilibrium Level

## Slide 28: Nonequilibrium Analysis of X2
Equilibrium Dominates
Nonequilibrium Dominates
Notes: Titan X2 nonequilibrium.xlsx

## Slide 29: Current issues of importance
Reaction rate for the excitation from ground state CN(X) to excited state CN(B).
Reaction rate for the dissociation of nitrogen
Experimental data from the EAST facility to confirm most relevant conditions from X2 data and to expand spectral range of experimental data.
Implementation of CR to full CFD

## Slide 30: Conclusion
Preliminary method for determining total capsule heat flux presented.
X2 testing bounds conditions of relevance to TiME.
X2 calibration verified by comparing equilibrium Mars radiation data with EAST and NEQAIR.
Effect of changes to important reaction rates shown.
Non-equilibrium parameter devised for future comparisons.
CR models and experimental results show a reduction factor of up to approximately 10 – 20 compared to results based on Boltzmann. Reducing total heat flux by approximately 50%.
Notes: Decay of Titan radiation found to be in good agreement between new simulations and experimental data.

## Slide 31: Questions?

## Slide 32: Titan Decay Rate
Titan decay rate analysis

## Slide 33: Nonequilibrium Analysis of X2

## Slide 34: Non-equilibrium Mars Calculations
Chris johnston vs mars X2

## Slide 35: EAST vs X2

## Slide 36: CFD Back Up
Atmospheric Composition
  CH4: 1.48%
  N2: 98.52%
Turbulence Model
  Baldwin-Lomax (Forebody)
Turbulent Schmidt Number: 0.5
14 species Gokcen models used
Fully catalytic radiative equilibrium wall boundary condition
Boltzmann distributions used for radiation